## Slide 1: Tomographic reconstructions under unknown angles and shifts
By Arunabh ghosh
Advisor: Prof. Ajit Rajwade

## Slide 2: Problem Statement
A standard problem in tomography is to reconstruct the object from a sample of its projections.
Tomographic reconstruction algorithms such as the filtered back projection algorithm assume that the angles at which the projection are taken are known and reconstruct the image successfully.
In some cases the projection angles may be unknown, for example when reconstructing certain biological proteins or moving objects.

## Slide 3: Moment based approach of estimating angles
The Helgasson Ludwig Consistency Conditions (HLCC) gives a relationship between the geometric moments of the underlying image and its projections.
These relations can be used to find out the unknown angles by iteratively solving for the unknown angles.
Using coordinate descent strategy we achieved a first estimate for the angles of the projection.
Unfortunately as moments are highly susceptible to noise, we need to further fine tune the estimates given by this algorithm.

## Slide 4: Fine tuning the estimates
To fine tune the estimates we decided to use alternate minimization to estimate the reconstructed image as well the angles at the same time.
For reconstructing the image, we formulated the problem as a compressed sensing problem assuming the image has a sparse basis in the DCT basis.
For estimating the angles we decided to coordinate descent on the projection angles, selecting the most optimum angle suiting the projection along that direction.

## Slide 5: Fine tuning of estimates – Reconstruction of Image
For estimating the image, we decided to formulate it as a optimization problem in the compressed sensing framework. The loss function is given by –
,
,
,
,

## Slide 6: Fine tuning of estimates – Estimate of angles
Taking the reconstructed image, fine tune on an angle estimate using the following algorithm:
  We assume the refined angle lies within a fixed delta of the original estimate. This delta depends on how noisy our projections are how off the original estimates are.
  Within this delta, we look for the most optimum angle, the projection along which (obtained from the latest reconstructed image) is closest to the actual observed projection.
We follow the above procedure for each of the angles, and obtain a new set of optimum angles.

## Slide 7: Fine tuning on the estimates
We follow the described procedure by first reconstructed image, followed by obtaining the angles estimates and we repeat this until the algorithm has converged and the difference in error is very small.
While optimizing on the angles, we define a fixed step size which defines with what precision we want to look into the delta space.
This parameter is decreased, to obtain greater precision in the theta estimates if we find the error hasn’t decreased in an iteration.

## Slide 8: Results
Environment conditions –
  Original image size – 80*80
  Noise in the projections – 5% Gaussian noise
  Angles are completely unknown
  In the next slide, we show the reconstruction results for a number of projection angles.
Original Image –

## Slide 9
Number of Projection Angles | Relative Error of moment based estimated image | Relative Error of moment based final image
20 | 15.47% | 10.54%
30 | 17.03% | 5.48%
50 | 2.99% | 0.22%
80 | 1.57% | 0.101%
Results

## Slide 10: Adding 50% noise to projections
We took the problem statement one step further, and decided to add 50% noise to the projections.
Our previous algorithm fails to reconstruct the image from such noisy projections.
So we had to modify the algorithm majorly focusing on how we can reduce the noise and make our algorithm robust to noise.

## Slide 11: Denoising of projections
The first step, involves using a patch-based PCA denoising method to reduce the noise in the projections.
However just this step is not enough to denoise in the projections.
We decided cluster the projections to a small set of projections using K-means clustering and take the cluster centres as our actual projections.
In the process of taking the cluster centres, the averaging over many projections would filter the noise out.
Taking the cluster centers our algorithm proceeded in the same way before.

## Slide 12
Number of Projection Angles | Number of Clusters | Relative Error of moment based estimated image | Relative Error of moment based final image
10000 | 50 | 28.26% | 28.92%
20000 | 50 | 17.43% | 14.14%
40000 | 50 | 14.56% | 13.1%
40000 | 90 | 12.35% | 9.54%
Results

## Slide 13: Some more results
Original Image Estimated Image Final Image

## Slide 14: Unknown shifts in Projections
Along with unknown angles, we now allow projections to have unknown shifts in them as well.
In Cryo-EM very often the projections are shifted by a small amount.
Having shifted projections seriously hamper our reconstruction results and give poor results.
We over here have developed algorithms to estimate these shifts, correct the projections and then reconstruct the image.

## Slide 15: Initial Estimate of Shifts
After a thorough survey of the literature, we learnt that shifts are mostly corrected by assuming that the center of masses of all projections should lie in the center, which makes sense for most objects as they would have the more mass near the center rather than the edges.
So we decided to shift the projections such that they have their center of masses at the origin.
This corrected some of the shifts but the results were not accurate enough to give good reconstruction results.

## Slide 16: Refining the shift estimates
We decided to incorporate the shift estimates in the Helgasson Ludwig Consistency Conditions (HLCC) themselves and we coordinate descended on the shifts as well as the angles.
The best shift was that shift which gave the lowest error in the error term formulated by the conditions.
This gave a reasonable shift estimate for all the shifts although we found that it required a lot of multi-starts to give us the best estimate.
We further pass these estimates to the alternate minimization scheme described above and try to correct for any erroneous estimate.

## Slide 17: Final shift estimates
Finally we incorporate the shift estimates in the alternate minimization scheme.
We construct the optimum image, and the optimum set of angles and assuming these to be true we decide the best shift estimate which reduces the error the most.
We repeat the above procedure for each projection.

## Slide 18: Results
Experiment conditions
  Size of original image – 80*80
  Number of projections – 50
  Noise in the projections – 5% Gaussian noise
  Angles – Unknown
  Maximum shift in the projections -
Relative error of estimated image | Relative error of final image
15.14% | 9.54%